## Slide 1: ESPR Abdominal (GI and GU) Imaging Task Force – recommendations in part together with ESUR paediatric urogenital imaging working group
Members (in alphabetical order, present chairs underlined):
Augdal TA, Avni FE, Bruno C, Damasio MB, Darge K, Franchi-Abella S, Herrmann J, Ibe D, Ključevšek D, Lobo ML, Mentzel HJ, Napolitano M, Ntoulia A, Ording-Müller LS, Perucca G, Petit P, Riccabona M, Smets AM, Stafrace S, Toso S, Woźniak MM
Former members: Blickman JH, Dacher JN, Littooij AS, Papadopolou F, Vivier PH, Watson T, Willi U
Booklet Editors: Riccabona M, Lobo ML

## Slide 2: ESPR Abdominal Task Force Group
The overarching aim of the ESPR Abdominal (GI & GU) Imaging Taskforce Group is to unite both expert- and less experienced radiologists, with a special interest in gastrointestinal and urogenital imaging in children
  Purpose: to facilitate personalized medicine, to improve quality, diagnostic efficacy & patient safety for pediatric GI & GU imaging through evidence and eminence based practice proposals
The ESPR Abdominal Task Force aims:
To elaborate, discuss & present new recommendations
To supplement existing recommendations for paediatric GU & GI imaging
  To provide guidance on how to adequately image children’s urogenital tracts & abdomen
  To standardise imaging which will improve quality & facilitate future meta-analysis to increase scientific evidence on how best to image the GI & GU tracts during childhood
To promote high level non-invasive imaging for neonates, infants & children
To provide support, education & refresher content + updates on state of the art paediatric radiology
To promote licensing of contrast media for use in children
  To spread knowledge on adaptations of imaging procedures for paediatric use
To foster multi-centre research on / data collection for paediatric uroradiology & abdominal topics
  e.g., collecting rare entities to increase knowledge & evidence
  e.g., to combine individual knowledge to optimised planned research on yet unanswered questions

## Slide 3: Introduction & general remarks
Recommendations & suggestions issued by ESPR Task Force
Consensus statements
  after thorough literature research & group & plenary discussions
    aiming at evidence-based practice
      which sometimes is scarce in paediatric imaging
    practical approaches – with room for adaptation to local needs & resources
Some of the statements are relatively old
  many still hold true & valid
  some have been intermittently readdressed & updated
    nevertheless - some may soon need adaptations to recent developments:
    revision = ongoing process (planned revisions are marked with )
    particularly indications may change & vary locally – so these were not always included
The task force was established to standardise & improve paediatric abdominal imaging
  the group first focused on GU tract in collaboration with ESUR paediatric working group
  then the work was extended to the entire paediatric abdominal imaging
  = new Task Force name „Abdominal (GI & GU) imaging“

## Slide 4: PART I: Procedural recommendations (listed in alphabetical order)
Recommendations issued for all major imaging modalities
Ultrasonography (including ce-US etc.), Fluoroscopy (mainly VCUG), plain film, IVU, CT, MRI
Also include respective interventions (e.g., renal biopsy)
All recommendations available as open access articles
Pediatr Radiol / Springer
ESPR Homepage: task force – abdomen (https://www.espr.org/taskforces/abdomen/ )

## Slide 5: „Anatomic“ paediatric MR-Urography (MRU)
Indications: e.g., malformation, obstructive uropathy, complicated infection, tumour, post-traumatic, cystic disease, renal transplant - previous US (+ reflux study, if indicated = VCUG, ce-VUS, RNC)
Preparation: general = place line in advance, consider creatinine for CA-studies (GFR), mock unit/visit to magnet hydration: NaCl/Ringer’s solution (20 ml/kg for 1 hour, max. 1000 ml), empty bladder before entering
priority to immobilization (feed & wrap)/no (minimal) sedation. Deep sedation only if needed
bladder catheter: deeply sedated patients who cannot empty bladder (if Furosemide given)
potentially also in high grade VUR with dynamic queries
catheter without balloon, urine bag, below level of MR table
diuresis: Furosemide 1 mg/kg IV (max. 20 mg), 15 min before beginning of investigation
timing may vary in dynamic-diuretic functional protocols (F -20, F -15, F 0, F +10, F +15, F +20)
MRU examination (anatomic – dynamic studies not well standardised, timing varies – not addressed)
positioning: supine position with arms above head, prone position if tolerated (for CA drainage)
SCOUT: sagittal important for correct oblique coronal plane, FOV: above diaphragms to below symphysis
potentially SSFP axial & coronal (+ sagittal)
heavily coronal T2-weighted sequences: eg. T2-3D TSE fs, 2D-thin/-thick slice [3D-UROGRAM], HASTE/RARE/PACE
T2-IR, unenhanced T1- & GRE sequence (3 slices anterior + posterior of kidneys for GRE; adjust FOV)
CA-application: only use cyclic Gd compounds (for MRA use motor pump & flow of 1 ml/sec)
repeated serial coronal T1-3D sGRE fs (for function continuously for 3-5min, subtraction particularly for MRA)
T1 (fs) axial & coronal, + sagittal if needed
coronal T1-3D GRE fs, additional delayed imaging up to 20(-30) min p.i., (possibly prone, postvoid – if necessary)
Abbreviations: CA = contrast agent, ce-VUS contrast enhanced voiding urosonography, FOV = field of view, fs = fat saturation, GFR = glomerular filtration rate, min = minutes, NaCl = saline, p.i. = post injection, RNC = radionuclide cystography, US = ultrasound, VCUG = voiding cysto-urethrography
Pediatr Radiol 2010;40:1315-1320

## Slide 6: Contrast-enhanced voiding urosonography = ce-VUS
Requisites: no diet restriction or enema, nor fluid intake for 2-3 hours, urine analysis.
Catheterism: feeding tube, 4-8 French, or suprapubic puncture
anaesthetic lubricant or coated paste
Note: latex free material in MMC patients…
Standard US of bladder & kidneys (supine, ± prone)
Bladder filling with NaCl infusion (only from plastic containers)
US- monitoring during filling, (potentially fractional) administration of UCA*
*or fill with NaCl–UCA solution (mostly SonoVue/Lumason, 0,2-5% concentration) as drip
Peri-/post-contrast US of bladder & kidneys (age adapted choice of transducer & frequency)
US modalities: fundamental, HI, CDS, low-MI contrast-specific methods
alternate scans of right & left side + bladder & retrovesical space during & after filling
During + after voiding : US of bladder & kidneys, + during voiding perineal US of urethra
supine ± prone, laying or sitting or standing
Indications: not defined, as they vary & may change
VUR diagnosis: echogenic micro-bubbles in ureters or renal pelves
Abbreviations: CDS = colour Doppler sonography, HI = Harmonic Imaging, MI = mechanical index, MMC = myelomeningocele, NaCl = saline, UCA = ultrasound contrast agent, US = ultrasound, VUR = vesico-ureteral reflux, 3DUS = three-dimensional ultrasound
Pediatr Radiol 2008:38:138-145, update 2013:43
*official SonoVue/Lumason dose:
1 ml/ bladder filling
alternative suggestion
(0.2)0.5-1(5)% of filling volume (fractional instillation) or
0,5-1% NaCl solution
Optison: (0,2-)0.5% NaCl solution

## Slide 7: CT in the paediatric urinary tract (uro-CT)
Indications: severe urinary tract trauma, complicated/equivocal urolithiasis & infection, tumour & DDx (particularly if no MRI), reno-vascular disease
Preparation: avoid pain, decrease anxiety, local protection device, generous immobilisation & sedation; do previous detailed US (except severe trauma)
for CA administration: previous line placement, hydration, consider measuring creatinine
Note: age dependent different normal creatinine values / GFR in infants & children
CA application 2.5-1.0 ml/kg (weight dependent); injection speed 1-2ml/sec (if power injector applicable)
age adapted injection rate & scan delay time - depends on:
location/size/type of IV access, child size/weight, underlying disease & query
Abbreviations: CA = contrast agent, DDx = differential diagnosis, GFR = glomerular filtration rate, IV = intravenous, KUB = kidney-ureter-bladder film, mSv = milli-Sievert, US = ultrasound
Pediatr Radiol 2010;40:1315-1320
Protocol: use age-/weight-adapted paediatric settings, restrict acquisition area (scout & scan!)
keep age corrected effective dose <2mSv, avoid multi-phase acquisitions (depends on query - unenhanced, arterial/cortical, nephrographic or excretory phase, potentially split bolus approach)
tailor protocols to query (according to clinical indication & result of previous US) plan/perform CT-study according to query/clinical indication, including one (or two/more) phases:
Note: only if high level US (+ KUB) not conclusive, always consider alternatively MRI
Nephrolithiasis
• unenhanced scan
• consider to further
reduce mAs,
• use low kV
Renovascular disease,
vascular malformation
• arterial phase/CTA
Trauma
• arterial phase: suspected vessel injury
not needed in split bolus protocol
• nephrographic phase: often sufficient,
always informative (split bolus protocol ?)
• urographic phase: suspected injury of
collecting system only (reduce exposition up to 50%)
Tumour, complication of infection, & DDx
• nephrographic phase: usually
sufficient, mandatory
• urographic phase: in selected
cases - assess involvement or
pathology of collecting system,
reduce dose

## Slide 8: Distal colostogram
Preparations: consider previous distal colon cleaning with enema (not for Hirschsprung)
skin markers on expected position of anus & existing perineal external orifices
Foley catheter (18French or higher) inserted into the stoma
balloon inflated & pulled back to maintain pressure or consider bandage to avoid spillage
Fluoroscopy: always start with lateral view, use pulsed fluoroscopy, proper use of shutters
add frontal view / oblique spot views, as needed - optional rotational 3D fluoroscopy
Documentation: last-image hold (pulsed fluoroscopy, if normal), spot films for pathology, keep video
distal colon length & calibre, distance from blind rectal pouch to anal dimple, fistula?
precise characterization (connecting structures, course, length, calibre)
Abbreviations: CA = contrast agent, H2O = water, I = iodine, ce-VUS = contrast enhanced voiding urosonography, VCUG = voiding cystourethrography
Pediatr Radiol 2017;47:1369-1380
Indications: anorectal & cloacal malformations, other specific case-based conditions
eg., after bowel perforation, Hirschsprung disease (for transition zone), colonic atresia
CA: water-soluble iodine contrast agent (100mg I/ml, or less) in infants
or barium in older children (if perforation / leakage not expected)
install by hand or instillation by infusion at 80-120 cm H2O
distal colon progressively filled under fluoroscopic guidance
maintain high pressure to allow for filling of potential fistula
proceed to genitography / fistulography &VCUG (ce-VUS) as needed
NOTE: all perineal orifices must be opacified in cloacal malformation

## Slide 9: Fluoroscopic genitography in infants
Indications: e.g., complex malformations, for surgical planning (preoperatively)
possibly at same session & using same catheter as for US-genitography (reduce invasiveness)
Preparation: vaginal catheterisation under sterile conditions
6-8 French feeding tube (thinner if urogenital sinus tract), avoid any air in catheter,
skin makers on perineal external orifices
Fluoroscopy: first assess pelvis for spinal / sacral abnormalities
before infusing CA
then: infuse /inject CA
water-soluble non-ionic CA, 100-150 mg I/ml, or even more diluted in NaCl
observe, take frontal, oblique & lateral views
documentation by last image hold & guided spot films (in pathology), keep video
in urogenital sinus tract / fistula: insert second catheter into urethra
if bladder fails to opacify
possibly blind catheterisation, curved tip catheter
Note: always first detailed baseline US, complemented by (ce-)US-genitography
proceed with VCUG thereafter for VUR evaluation - to complete study if needed / indicated
Abbreviations: CA = contrast agent, I = iodine, NaCl = saline, US = ultrasound, VCUG = voiding cystourethrography, VUR = vesico-urethral reflux
Pediatr Radiol 2014;44:496-502
Technique: only use pulsed fluoroscopy (avoid C-arm)
proper use of filters, grid, shutters (not electronic margins)

## Slide 10: Intravenous urography (IVU) in childhood
Preparations: age = minimum 4-6 weeks, in infants perform before next meal
NPO, hydration, creatinine, venous line
Procedure: adapt exposure & CA to age / weight
proper use of filters, grid, shutters (not electronic margins)
renal area, or KUB (include symphysis)
initial KUB only if indispensable (e.g., urolithiasis)
reduce number exposures, e.g.:
one early renal view at 5 minutes
single late KUB at 15-20 minutes
additional focused images, if needed for treatment
diuretic IVU: Furosemide iv. 1 mg/kg BW (max. 20 mg) 20 min before exposure
inject 5 minutes before, with, or 5-10 minutes after CA application
Goal: answer specific query with minimal radiation (ALARA)
Abbreviations: BW = body weight, CA = contrast agent, iv. = intravenous, KUB = kidney ureter bladder film, NPO = nothing peroral, US = ultrasound
Pediatr Radiol 2010;40:1315-1320
Note: avoid multiple, unnecessary or particularly tomographic views
Indications: in exceptional cases, no access to MRU/CT, equivocal findings on US & pre- or/and post-operative, urolithiasis, (trauma – e.g. after CT), caliceal diverticula, ureteral & subtle caliceal pathology
Note: previous dedicated US study mandatory
IV. contrast dose
Age [year] ml/kg BW
1 2.5
2 2.0
3 1.5
>4 1.0

## Slide 11: Neonatal female genital ultrasound
Requisites: well hydrated, full bladder, adequate equipment & transducers
full bladder: consider NaCl-filling through small (4-6 French) catheter if needed
Note: include US of entire urinary tract + adrenal glands (potentially add spinal cord US) (additional) abdominal survey useful using high resolution linear transducer
consider perineal & trans-symphyseal approach
Standard US - abdominal approach:
assess uterus (with cervix), vagina, ovaries
present? size, morphology, position, vaginal / uterine obstruction?
assess bladder (with distal ureters) + retrovesical space, potentially labia (ectopic gonads?)
Abbreviations: DSD = disorder of sexual development, NaCl = saline, iv. intravenous, (3D)US = (three-dimensional) ultrasound
Pediatr Radiol 2014;44: 496-502
Potentially proceed with US-genitography:
one may add 3DUS + coronal reconstructions (thick slab)
for better definition & characterisation of uterine & vaginal anomalies (visualise coronal plane)
Perineal US: vagina (& urethra), cervix (potentially + anal canal)
morphology, position, patency, after filling & during voiding
if obstruction: distance from lowest end to perineal orifice
Indications: suspected malformations, other condition with potential genital involvement
eg., single kidney, cloacal malformation, DSD …

## Slide 12: Paediatric gastrointestinal (bowel) ultrasound (GI-US)
Examination: targeted examination (POCUS) or detailed general assessment
overview = convex probe
detailed analysis of bowel (wall) = high resolution linear transducer
following bowel easier in organo-axial sections, complete by longitudinal sections
(gentle, but persisting) graded compression
Harmonic Imaging helpful, CDS sometimes essential
possibly fill & distend structures (drinking fluid, instillation via gastric tube, saline enema)
for lesser pelvis / anorectal region: perineal approach
documentation sometimes challenging – use pictograms, possibly extended view, dual image, representative & repeatable sections, sometimes clips & M-mode useful (e.g., peristalsis)
Requisites: no preparation, sometimes fasted before drinking / filling helpful
range of transducers with variable (high) frequencies (curved array & linear transducer)
Note: saline, milk (stomach) or UCA may serve as agents
some use formula as for MR-enterography for small bowel distention
Indications: many accepted, sometime childhood specific queries:
e.g., hypertrophic pyloric stenosis, malrotation & volvulus, appendicitis, intussusception, Inflammatory bowel disease, duplication cysts, mesenteric lymphadenopathy, necrotizing enterocolitis & intestinal pneumatosis, microcolon, gastro-oesophageal reflux & hiatal hernia (specific protocol), polyps & tumours
used for initial diagnosis, assessment of complications, & follow-up
Abbreviations: CDS = Colour Doppler sonography, POCUS = point of care US, US = ultrasound, UCA = ultrasound contrast agent
Pediatr Radiol 2018;48:1528-1536
Note: always complete by abdominal survey

## Slide 13: Paediatric urosonography
Requisites: well hydrated patient, full bladder, adequate equipment & transducer
Urinary bladder: start with bladder, observe size (capacity), shape, ostium, wall, bladder neck
include distal ureter & retrovesical space/inner genitalia, urachus?
optional: CDS for urine inflow, perineal US, scrotal US …
Kidneys: lateral and/or dorsal, longitudinal & axial sections
parenchyma, pelvi-caliceal system, size & symmetry
standardised measurements in 3 dimensions & volume calculation
if dilated: maximum axial pelvis & calix diameter, narrowest parenchymal width, + PUJ
optional: (a)CDS & duplex-Doppler, potentially ce-US (e.g. DDx of cysts…) …
during voiding: potentially urethral imaging (perineal approach?), change in pelvi-caliceal or ureteral size?
Post void evaluation:
bladder: residual volume, bladder neck, shape & configuration
kidneys: dilatation of pelvi-caliceal system / ureter changed?
optional: ce-US, ce-VUS, 3DUS …
Additional abdominal US survey recommended
Abbreviations: (a)CDS = (amplitude coded)colour Doppler Sonography, ce-US = contrast-enhanced ultrasound, DDx = differential diagnosis, PUJ = pelvi-ureteric junctions, US = ultrasound, 3DUS = three-dimensional ultrasound, ce-VUS = contrast-.enhanced voiding urosonography
Pediatr Radiol 2008;38:138-145
Indications: numerous – not detailed

## Slide 14
Pelvic MRI in ano-rectal & cloacal malformations
Technique: multi-planar T2 SE, T1 pre- & post-Gd
at least 2 planes, slice thickness 2-3 mm or less, no fs - except (ce-)T1
also in excretory phase to look for ureters, or after MRU
HR isotropic 3D-MRI sequences in T2 & (ce-)T1
dynamic cine (ce-)T1 (or T2) during active filling into stoma & common channel
include pelvic floor MRI & (distal) spine MRI
consider previous MRU (or at least coronal T2 and T1 after Gd)
Post processing: meticulous post processing & images analysis
interpretation in accordance with previous imaging studies
potentially 3D-reconstructions, multi-planar reformatting & rendering
Abbreviations: ce = contrast enhanced, fs = fat saturation, Gd = Gadolinium, HR = high resolution, IV. = intravenous, MRU = MR-Urography, NaCl = saline, SE = spin echo, 3D = 3-dimensional
Pediatr Radiol 2015;45:2023-2028
Indications: complex anorectal /cloacal malformations, other complex genital malformations
Preparation: deep sedation / general anaesthesia support – often required
skin markers (capsules or similar) on expected position of anus & other perineal orifices or catheters left in place as localizer & for dynamic study
iv. peripheral line access
filling of pelvic structures with NaCl (T2) and/or diluted Gd 1:1000 (T1)
of common channel via feeding tube (6 French or less)
of distal colon via Foley catheter, balloon inflated within stoma to avoid spillage of urinary bladder via vesicostomy or catheter

## Slide 15: Renal iv. contrast-enhanced ultrasound (renal CEUS)
Requisites: no diet restriction or enema, large line without filters, safety precautions
Note: informed consent necessary – presently off-label use
Indications: to list some - renal trauma & vessels, renal masses (particularly complicated cysts), infarction / organ, perfusion, infection, renal transplant
Standard US of kidneys: supine ± prone, sagittal & axial
include bladder, include abdominal survey and (a)CDS
UCA application: e.g. SonoVue® (Optison®) iv. - slow injection + (abundant) saline flush
potentially repeated administration, reperfusion imaging after burst, start clip with timer clock
Abbreviations: (a)CDS = (amplitude-coded) colour Doppler sonography, HI = Harmonic imaging, iv. = intravenous, MI = mechanical index UCA = ultrasound contrast agent, US = ultrasound
Pediatr Radiol 2014;44:1478-1484 and Pediatr Radiol 2018;48:1528-1536
Peri-/post-contrast renal US: supine ± prone, sagittal & axial
US modalities: HI, low MI contrast-specific methods
alternate scans of right & left side, may use 1 dose/kidney
time window: up to max. approx. 5 minutes, usually 2-3 min
Dose SonoVue® (Bracco / Italy) (suggestions from experience, no dose finding studies)
first year(s) = 0,03-0.1 ml/kg SonoVue®
3 – 15 years = 0.06 ml/kg SonoVue® / or: ml of SonoVue® = age in years/20, some use 0,1 ml/year
maximum adult dose: 4.8 ml = 2x2.4 ml SonoVue® (≈ 0.05-0,1 ml/kg)
Paediatric liver dose for Lumason (Bracco / USA – presently the only approved application) = 0.03 ml per kg

## Slide 16: Renal biopsy in childhood
Requisites: pre-interventional detailed US of entire abdomen (with CDS)! time out! team approach
location: procedure room, monitoring & resuscitation facilities, empty bladder, anaesthetic paste
sedation: depends on age state: <12 y = deep sedation + local anaesthesia
>12 y = conscious sedation + local anaesthesia have iv. line in place, oxygen & suction facilities at hand , monitor BP, HR, O2-saturation, pCO2
Instrumentation: (matching / automatic) biopsy gun / semi-automatic biopsy needle
details decided on pre-interventional US (eg. parenchymal thickness): needle length = 13-20 cm
calibre = 20-18 Gauge (some use 16-14 G, but higher risk), sample length = 1.2/1.5/2.2 cm
coaxial technique if difficult, deep, obesity … (insert guiding needle just till renal capsule)
material: disinfection, local anesthesia, skin incision, sterile cover/utensils, sample handling material,
US equipment - optimal transducer for patient’s size, sterile wrap; potentially microscope
Abbreviations: AVF = arteriovenous fistula, CDS = colour Doppler sonography, BP = blood pressure, HR = heart rate, US = ultrasound
Pediatr Radiol 2014;44:496-502
Procedure: initial orienting US (bladder empty?), sedation
patient positioning (native kidney = prone, rTx = supine), disinfection, local anaesthesia
target lower pole of left kidney if possible - US localization + external marking (CDS for vessels)
biopsy shot after skin incision & needle placement, real time documentation
evaluation & inspection of specimen - repeat if necessary, keep number of passes low
immediate post-biopsy US (document biopsy site, potential hemorrhage &“macro”-AVF)
Post biopsy measures: effective compression of biopsy site, standardized monitoring
as for following interventional procedures with potential vascular complications
e.g., bleeding / macrohaematuria, hypovolemia, hypertension-BP management
rescan after 4-6 hours and/or 12-24 hours after biopsy, always include CDS
prolonged monitoring & rest in complications (significant bleeding, AVF)
Note: there may be local variations in the handling
Indications: not defined, as they vary & may change

## Slide 17: Retrograde urethrography
Preparations: urine sample (urine sterile?)
Catheterisation: Foley balloon catheter, sterile technique
less common feeding tube - applying manual compression to seal meatus
Procedure: inflate catheter balloon (or manual compression at meatus)
use 1-2 ml for balloon inflation in navicular fossa, fluoroscopic guidance
install CA – slowly under fluoroscopic monitoring
dilute water-soluble ionated CA (100-150 mg I / ml) in NaCl
careful fluoroscopic examination
document by last image hold and/or focussed exposures
at least 2 planes, potentially additional oblique views
Documentation: last-image hold (if urethra normal)
spot films for pathology:
e.g., stricture, stenosis , fistula, discontinuity, CA extravasation, diverticulum, utricle, duplication, other malformation
dynamic changes (during filling or voiding): keep video clip (of fluoroscopy or ce-US)
Abbreviations: CA = contrast agent, NaCl = saline
Pediatr Radiol 2015;45:2023-2028
Indications: urethral trauma, stricture or stenosis, rare malformations, urethral fistula, utricle
Technique: only use pulsed fluoroscopy (avoid C-arm)
proper use of filters, grid, shutters (not electronic margins)

## Slide 18: Sonographic (ultrasound) genitography
Procedure: NaCl filling by continuous infusion
to compensate vaginal leakage, to get rid of vaginal air possibly rectal NaCl enema
e.g., to assure uterine agenesis, complex malformations & ARM, fistula
in urogenital sinus tract (if bladder empty/fails to fill)
insert 2nd catheter (sometimes blind with curved tip) anteriorly into urethra / bladder
assess continuously - using abdominal, trans-symphyseal & perineal approach
also include kidneys / urinary tract, potentially add 3DUS
possibly add UCA: for detecting connections, fistula, assess vaginal duplications …
UCA dose as for ce-VUS (varies also with frequency used & US device, 0.5-1-5% NaCl solution)
Abbreviations: ce-VUS = contrast-enhanced voiding urosonography, NaCl = saline, UCA = US contrast agent, (3D)US = (three-dimensional) ultrasound
Pediatr Radiol 2014;44:496-502
Indications: genital malformations, ambiguous genitalia, work up of syndromes & anorectal malformations, equivocal findings on baseline US
Note: sometimes previous bladder filling (catheterisation to fill) for US access
and rectal tube (for saline enema to identify rectum) helpful / necessary
Note: always first detailed baseline US, including urinary tract US (+ spinal US)
Preparation: vaginal catheterisation under sterile conditions
6-8 French feeding tube (thinner if urogenital sinus tract), avoid any air in catheter
Proceed with ce-VUS thereafter for VUR evaluation - to complete study if needed / indicated

## Slide 19: Voiding cysto-urethrography= VCUG
Requisites: no diet restriction or enema, urine analysis, potentially antibiotics
potentially no fluid intake for 3 hours
Catheterism: catheter / (feeding) tube, 4-8 French, or suprapubic puncture
Note: latex precaution particularly in neural tube defect patients, bladder exstrophy
Fluoroscopic view of bladder & renal fossa (initial + during early filling)
Bladder filling with radiopaque CA, observe with intermittent pulsed fluoroscopy views
gravity drip = bottle ≈40 cm above table, watch dripping to guide fluoroscopy, AB?
Fluoroscopy if signs of increased bladder pressure, imminent voiding, urge …
bilateral oblique views of distal ureters, include catheter, document VUR,
include kidney (exposure for intra-renal reflux)
After voiding : ap view of bladder & renal fossae; assess CA drainage from kidney if refluxed
Abbreviations: AB = antibiotics, CA = contrast agent, US = ultrasound, VUR = vesico-ureteral reflux
Pediatr Radiol 2008;38:138-145
When voiding : remove catheter, unless cyclic VCUG = 3 fillings in 1st yr(s) - then removed in last cycle
female: 2 spots/exposures of distended urethra (slightly oblique)
male: 2-3 spots/exposures during voiding (ap & high oblique / lateral)
include renal fossae during voiding, if VUR => spot film/exposure for intrarenal reflux
Note: VUR grading, post investigational antibiotic prophylaxis?
Technique: only use pulsed fluoroscopy (avoid C-arm), + exposures in case of high degree VUR & urethral details, proper use of filters, grid, shutters (not electronic margins)
Indications: under discussion- vary regionally 6 may change

## Slide 20: Part II: Imaging algorithms (listed in alphabetical order)
These recommendations aim at
standardising imaging algorithms for comparability
  however, adaptable to local needs & resources
quality assurance – also considering efficacy aspects
optimising dose in terms of radiation protection / awareness
Recommendations issued for all major queries
ano-rectal & genital malformations (including ambiguous genitalia), biliary atresia, cystic kidney disease, (foetal) PCD/UTD & obstructive uropathy, (micro)haematuria, renal transplantation, reno-vascular hypertension, scrotal swelling, testicular microlithiasis, (scrotal & ovarian) torsion (including scrotal swelling), urolithiasis, urinary tract infection, urinary tract trauma
Abbreviations: PCD = pelvicaliceal distension / dilatation, UTD = urinary tract dilatation

## Slide 21
Imaging in newborn with anorectal malformation (ARM)
Plain films: chest, spine & pelvis, abdomen
+
US: abdomen & pelvis & spine
Detailed pelvic US, +/- US genitography / ce-VUS / fistulography
Distal colostogram, +/- fluoroscopic genitography/fistulography + VCUG (ce-VUS)
Pelvic MRI
+ MRU, … others as needed (CT only for very selected cases)
Question: high / low ARM, Colostomy?
+/- genital malformation, bladder drainage?
0-3 days
1-3 months - delayed imaging work-up, prior to definitive surgery
if further imaging needed
Pediatr Radiol 2017; 47:1369–1380
Abbreviations: ce-VUS = contrast-enhanced voiding urosonography, MRI = Magnetic resonance imaging, MRU = magnetic resonance urography, US = ultrasound, VCUG = voiding cystourethrography,

## Slide 22: Imaging algorithm in suspected biliary atresia (BA)
Abbreviations: BA = biliary atresia, ERCP = endoscopic retrograde cholangio-panceraticography, GBA = gall bladder anomalies, PTCC = percutaneous transhepatic cysto-cholangiography, TCS = triangular cord sign, US = ultrasound
Pediatr Radiol 2020;50:in press
Indications: based on clinical /laboratory findings: conjugated hyperbilirubinaemia +/- acholic stools
US (GBA, TCS, cyst, Doppler, elastography)
Dilation of intrahepatic bile ducts
= BA ruled out =
stop & respective imaging
Suggestive findings & syndromic presentation = high suspicion
Normal findings
<30 days
weekly US & biological test
>30 & <60 days
Normal
Equivocal findings
very young child with partially acholic stools, atypical patterns suggestive of medical causes
PTCC or ERCP
+
liver biopsy
Stop
when cholestasis has resolved
No BA
BA
Surgery

## Slide 23: Imaging in childhood urinary tract infection (UTI)
UTI *1
US + aCDS
pyo(hydro)nephrosis
→ nephrostomy
if no response to AB
normal US
clinically cystitis
stop
follow-up US?
if clinically clear + known normal urinary tract anatomy => no imaging necessary?
only delayed imaging for scaring in upper UTI?
follow-up US (in complicated course, or after 4-6 weeks)
complications: respective sectional imaging if unclear on US
VUR-evaluation (often based on individualised multidisciplinary decision), always in infants, + recurrent febrile confirmed UTI in >2 y
  ce-VUS: in girls (if available),or VCUG (e.g. in boys & preoperatively, complex …)
for VUR follow-up: ce-VUS or RNC (if available)
scars: late DMSA or (functional) renal MRI (after 4/6-12 months)
bladder function studies (>5 y, urodynamics)
(pyelo)nephritis *2
aPN / upper UTI / scar
*2 DDx: Tu / cyst versus abscess & similar
complicated UTI (e.g., XPN, Tbc)  MRI/CT
*1 UTI criteria: urine sample (catheter, culture!) & blood count
within first days
particularly in severe symptoms
acute DMSA
or renal MRI with DWI
normal US, but clinically upper UTI
  - no aCDS
  - aCDS equivocal *2
normal
Pediatr Radiol 2008; 38: 138–145
Abbreviations: AB = antibiotics, aCDS = amplitude coded colour Doppler sonography (= “power Doppler”), (a)PN = (acute) pyelonephritis, ce-VUS = contrast-enhanced voiding urosonography, CT = computer tomography, DDx = differential diagnosis, DMSA = static renal scintigraphy, DWI = diffusion weighted imaging, MRI = magnetic resonance imaging, RNC = radionuclide cystography, Tbc = tuberculosis, Tu = tumour, US = ultrasound, VCUG = voiding cystourethrography, VUR = vesico-ureteric reflux, XPN = xanthogranulomatous pyelonephritis

## Slide 24: Imaging in mild foetal pelvi-caliceal distention (PCD)
antenatal diagnosis of mild to moderate PCD
abnormal: pelvis 7(10) mm + dilated calices ( PCD III*1), or other anomalies
normal
normal
US at 1 mo
US at 3 mo
pelvis 10 mm
otherwise normal
stop follow-up
further morphological & functional evaluation: scintigraphy, (IVU), MRU …
respective follow-up & treatment
US: 1st US around day 5
normal
stop follow-up
abnormal
pelvis 10 mm, PCD III
other malformation & changes
- “extended criteria” *
VCUG
or ce-VUS (particularly in girls)
Pediatr Radiol 2008; 38: 138–145
Abbreviations: ce-VUS = contrast-enhanced voiding urosonography, IVU = intravenous urography, MRU = magnetic resonance urography, PCD = pelvi-caliceal distension (*1 according to the ESPR Taskforce grading system), US = ultrasound, VCUG = voiding cystourethrography
* “extended criteria”: additional to dilatation - bladder pathology (thick wall, trabeculation, diverticula, bladder neck? ), ureteral abnormalities (dilatation, wall, ostium, peristalsis, duplex), renal parenchymal changes (cysts, dysplasia, narrowing, poor differentiation etc .), urothelial sign (ureter / pelvis)
indication for VCUG under discussion & changing

## Slide 25: early US + VCUG / ce-VUS *
PUV
obstructive uropathy
high grade VUR
UPJO, MU *5
 drainage, renal function?
+ scintigraphy *2, MRU *3
US follow-up
at 6 months: isotopes *2, MRU*3 ?
others *4
as indicated *5
*1 (US) genitography: in patients with single kidney, multicystic dysplastic kidney (MCDK), ectopic kidney, suspected genital anomaly
*2 MAG3 – better than DMSA scintigraphy in dilated systems & neonates, DMSA usually after > 3-6 months, not before 6 weeks;
+ open bladder catheter to avoid VUR induced errors
*3 MRU – for complex anatomy, function, obstructive component
*4 e.g.: multicystic dysplastic kidney (MCDK), cystic dysplasia, duplex / horseshoe kidney, other malformation, non-obstructive PCD, cysts/cystic tumor
*5 see respective algorithm
(Postnatal) imaging in newborns with foetally diagnosed high grade pelvi-caliceal distention (PCD)
* VCUG in all boys (for PUV)
particularly if ureter dilated
ce-VUS in girls, potentially delayed
+ narrowed or dysplastic parenchyma, dilated ureter
particularly if bilateral or single kidney*1
Prenatal US: gross dilatation = PCD ≥IV° *1
Pediatr Radiol 2009; 39: 891–898
Abbreviations: ce-VUS = contrast-enhanced voiding urosonography, MAG3 = dynamic-functional renal scintigraphy, MRU = magnetic resonance urography, MU = megaureter, PCD = pelvi-caliceal distension (*1 according to the ESPR Taskforce grading system), PUV = posterior urethral valve, UPJO = ureteropelvic junction obstruction, US = ultrasound, VCUG = voiding cysto-urethrography, VUR = vesico-ureteric reflux
indication for VCUG under discussion & changing

## Slide 26
US (+ Doppler)
US follow-up
hydration! Doppler!
diuretic US (?)
mild (PCD <III°) x1
< 6 weeks old
VCUG (ce-VUS?)
VUR/PUV x1
no VUR
MAG3 scintigraphy (T+20) x4
or (quantitative) MRU
or IVU (pre-operative, if no MRU)
obstructive,
low function
 OP (>3-6 months)
equivocal - also, if <3 months + obstructive & normal function
>6 weeks old
potentially diuretic US(?)
deteriorationx2
clinical symptoms x3
non-obstructive
normal function
VUR?
others x1
 MAG3 renal scintigraphy (T-20), follow-up (after 3-6 mo)
Imaging algorithm in infants & children with suspected obstructive uropathy
x2 Proposed imaging criteria for deterioration: on MAG3 decreased (split) renal function & drainage, contra-lateral hypertrophy, on US increasing dilatation, decreasing parenchymal width, echotecture, contra-lateral hypertrophy (+ decreased vascularisation, asymmetrically elevated Resistive Index, reduced peristalsis in MU and/or ureteric jet - asymmetrically in unilateral disease)
x3 Clinical criteria for deterioration: pain, infection, haematuria, (kidney) growth failure, hypertension
clinical symptoms x3
x1 as appropriate, see also respective algorithm
PCD ≥III°
x4 assess drainage pattern and (split renal) function
Pediatr Radiol 2009; 39: 891–898
Abbreviations: ce-VUS = contrast-enhanced voiding urosonography, IVU = intravenous urography. MAG3 = dynamic-functional renal scintigraphy, MRU = magnetic resonance urography, MU = megaureter, OP = surgery, PCD = pelvi-caliceal distension (according to the ESPR Taskforce grading system), PUV = posterior urethral valve, US = ultrasound, VCUG = voiding cysto-urethrography, VUR = vesico-ureteric reflux
indication for VCUG under discussion

## Slide 27
Imaging algorithm for suspected urolithiasis in childhood
US (gray scale + DDS / CDS)
x1 or KUB (+ adapted IVU, particularly if low-dose CT unavailable)
positive
negative + low clinical suspicion
x2 potentially contrast-enhanced CT-urography, if other DDx or complication; MRU in selected cases
inconclusive US
US non-diagnostic
mismatch US & clinics
negative +
high clinical
suspicion
Stop
uro-CT x1
(ultra-)low dose + unenhanced x2
only 2nd signs + no stone visible
or before intervention, if therapeutically necessary
+ KUB (± IVU) before intervention / lithotripsy
potentially + KUB for
confirmation, for treatment…
follow-up after/ /during treatment
+ KUB*3
Pediatr Radiol 2009; 39: 891–898
Abbreviations:, uro-CT = urinary tract computed tomography, CDS = colour Doppler sonography, DDS = duplex Doppler sonography, DDx = differential diagnosis, IVU = intravenous urography, KUB = Kidney Ureter Bladder radiograph, MRU = magnetic resonance urography, US = ultrasound
x3 KUB for confirmation, planning radiographically guided lithotripsy, potentially for localization & depiction of ureteric stones

## Slide 28
Imaging algorithm for haematuria in infants & children
abscess, pyohydronephrosis,
severe haemorrhage …
 intervention *4
US + DDS/(a)CDS
US normal
*4 DD: tumour, haemorrhage, complicated UTI
e.g., XPN, Tbc, abscess → MRI/CT
diagnosis evident
Clinical & laboratory evaluation *
= presumable diagnosis in most situations
*2 see respective dedicated imaging algorithm
potentially further imaging
depending on clinical course & query*3
+ basic imaging:
*1 Examples: UTI, UPJO, VUR, MU, urolithiasis *2
tumour , GN & nephropathies, bladder-, urethral- , ureteral pathology *3
trauma and vascular disease *2,3.
US inconclusive or
mismatch US & clinics
*3 proceed to next imaging step (MRI / CT, Angiography, VCUG, scintigraphy etc. - as indicated )
* clinical & laboratory evaluation: variation (day time, position, activity)? vaginal/rectal discharge? duration? recurrent? undulating symptoms? pain or colic? trauma? fever? dysuria? age (foreign body)?, blood pressure? microscopic or macroscopic haematuria? family history? urinalysis (erythrocyte morphology, isolated hematuria? ), renal function? blood count / CRP etc.
Note: malignancy much rarer than in adults
Stop imaging
 further imaging as appropriate
if necessary *1
Haematuria
Pediatr Radiol 2009; 39: 891–898
Abbreviations: ce-VUS = contrast-enhanced voiding urosonography., CRP = C-reactive protein, CT = computed tomography, DDS = duplex Doppler sonography, (a)CDS = (amplitude-coded) colour Doppler sonography, MRI = magnetic resonance imaging,, MU = megaureter, Tbc = tuberculosis, US = ultrasound, UTI = urinary tract infection, UPJO = uretero-pelvic junction obstruction, VCUG = voiding cysto-urethrography, VUR = vesico-ureteric reflux, XPN = xanthogranulomatous pyelonephritis

## Slide 29
*9
*8
*7
*6
minor trauma (= low pretest probability)
Note: renal trauma more common in children
degree of hematuria not reliable, hypotension = late sign
US + (a)CDS *1
ce-CT*2,3
surgery, intervention *4…
follow-up US + (a)CDS *5
in 6-24h, potentially clinical observation?
additional imaging as needed
MR, ce-CT, angiography, (DMSA)
*1 examination of entire abdomen & pelvis, if available potentially ce-US
*2 see previous procedural recommendation
*3 for bladder injury query: VCUG - late phase ce-CT/ CT-CG, only if CT done for other reasons
*4 for vascular injury with therapeutic options
*5 US + (a)CDS (potentially ce-US) = first choice for follow-up, if vascular complications suspected => angiography & embolization
potentially MR – especially for late presentation & follow-up - avoid repeated unnecessary CT’s !
*6 if therapeutic impact &/or high probability of associated injuries
*7 if severe vascular injury …
*8 conservative treatment, low suspicion of other injuries
*9 depends on severity of findings = if no treatment needed
minor pathology
normal
severely abnormal*3
inconclusive US
high probability of additional injury, clinical discordance &/or deterioration, no reliable US available + no clinical observation planned
stop
*8
Abbreviations: (a)CDS = (amplitude-coded) color Doppler sonography, ce-CT= contrast-enhanced computed tomography; ce-US = contrast-enhanced ultrasound;, CT-CG = CT-cystography; DMSA = Dimercaptosiccinidacid static renal scintigraphy, MR = magnetic resonance; US = ultrasound; VCUG = voiding cystourethrography
Imaging algorithm in mild pediatric urinary tract trauma
Pediatr Radiol 2011; 41:939–944

## Slide 30
*1 rapid deceleration injury, direct flank injury, fall from height
*2 examination of entire abdomen & pelvis, if available potentially ce-US
*3 see previous procedural recommendation
*4 for bladder injury query: VCUG, late phase ce-CT/ CT-CG, only if CT done for other reasons
*5 US + (a)CDS (potentially ce-US) = first choice for follow-up, if vascular complications suspected => angiography & embolization,
potentially MR – especially for late presentation & follow-up - avoid repeated unnecessary CT’s !
Abbreviations: (a)CDS = (amplitude-coded) color Doppler sonography, ce-CT= contrast-enhanced computed tomography; ce-US = contrast-enhanced ultrasound; CT-CG = CT-cystography; DMSA = Dimercaptosiccinidacid static renal scintigraphy, FAST = focused assessment with sonography for trauma; MR = magnetic resonance; US = ultrasound; VCUG = voiding cystourethrography
major trauma*1 (= high pretest probability) & polytrauma
Note: renal trauma more common in children, degree of hematuria not reliable, hypotension = late sign
Imaging algorithm in severe pediatric urinary tract trauma
(direct impact only to kidney & high quality US available)
stable
unstable
US + (a)CDS*2
surgery
ce-CT*3,4
“FAST”
interventional / angiography
for vascular injury with therapeutic options …
(“FAST”)
follow-up US + (a)CDS *5
additional imaging as needed
MR, ce-CT, angiography, (DMSA)
Pediatr Radiol 2011; 41:939–944

## Slide 31
inconclusive US or no signs of RVD
diagnosis evident
RAS
DDS criteria: PSV >180-200 cm/sec
Note: age variations
RAR >3.5, δ-RI >0.05
Acceleration time >80msec
Tardus-Parvus pattern distally
other causes
further imaging
as appropriate *
DSA with simultaneous PTA
(potentially + renal vein sampling)
stage 1 hypertension
or BP well controlled on 1-2 drugs
stage 2 hypertension
BP not controlled by 2 or more drugs,
stage 1 age <3y, or high clinical suspicion*1
CTA
or Captopril renography*3/MRA*2
RVD
normal
clinical follow-up
DSA + renal vein sampling
potentially simultaneous PTA
high clinical suspicion*1
* Further imaging as appropriately indicated (see existing recommendations …)
*1 High clinical suspicion: history of renal trauma or radiation, umbilical artery catheterization, renal vascular thrombosis, bruit over renal arteries, high renin levels, presence of disease associated with renovascular pathology (e.g., neurofibromatosis, Williams’ syndrome, tuberous sclerosis …)
*2 MRA: potentially & increasingly ce-MRU for large vessels & infarcted areas, non-enhanced MRA techniques?
*3 Captopril scintigraphy: potentially prior to PTA for function, particularly in doubtful situations or neonates until old enough for PTA, Note: local variations
Abbreviations: BC = blood count, BP = blood pressure, BUN = blood urea nitrogen, CDS = colour Doppler sonography, cm/sec = centimetres per second, CTA = CT-angiography, DSA = digital subtraction angiography, DDS = spectral duplex Doppler, MRA = MR angiography, PSV = peak, systolic velocity, PTA = percutaneous transluminal angioplasty, RAR = renal aortic ratio, RAS = renal artery stenosis, δ-RI = Resistive Index difference, RVD = renovascular disease, US = ultrasound, y = year
Imaging in potential childhood reno-vascular hypertension
renal US + CDS & DDS
Basic clinical & laboratory evaluation: BP both arms + one leg, repeated BP / 24 hour BP monitoring (age related chart), retinal examination, echocardiography, chest X-rays. BUN, creatinine, electrolytes, urinalysis, urine culture, BC
validate indication
suspected reno-vascular hypertension
Pediatr Radiol 2011; 41:939–944

## Slide 32
Typical male anomalies:
undescended testis
congenital hydrocele
inguinal hernia
cystic dysplasia of rete testis
cystic dysplastic seminal vesicles
intersex = refer to dedicated centre
others: hypospadia, torsion, inflammation
Scrotal US (+DDS)
+ inguinal & pelvic US
Usually diagnosis evident
+ US of the urinary tract*
normal
abnormal
inconclusive
further imaging very rarely needed
? MRI / VCUG for complex / combined malformation
* including adrenal US
search for associated malformations
US early follow-up
Imaging of neonatal & infant male genitalia
Abbreviations: DDS = Duplex Doppler sonography, MRI = magnetic resonance imaging; US = ultrasound; VCUG = voiding cystourethrography
Pediatr Radiol 2014; 44:496–502

## Slide 33
Scrotal swelling in the neonate
(IMMEDIATE) SURGICAL EXPLORATION
Lack of testicular flow
Hydrocele
Transilluminant
Not transilluminant
Follow up US?
Necrosis*
No surgical emergency
Reduced testicular flow and/or twisted spermatic cord / funiculum
Bilateral or possibly vital testicular tissue*1
Extra-testicular cause of scrotal swelling or suspected Tumour
or
* Mixed echogenicity with necrotic areas, possible calcifications, avascular (sometimes indistinguishable from teratoma --->follow up US)
*1 Visualisation of some normal or oedematous testicular tissue, perfused areas …
Inguinal & scrotal US (+ CDS/DDS)
Note: In torsions present at birth testicle almost never salvageable - in neonatal torsion (<30 d after birth) testicle more often salvageable
Pediatr Radiol 2015; 45:2023–2028
Abbreviations: CDS = Colour Doppler Sonography, d = day(s), DDS = Duplex Doppler Sonography, US = ultrasound (high resolution, linear transducer!)

## Slide 34
Suspected testicular torsion in children >1 month
Symptoms <24h
+ typical age +
≥1 typical clinical sign*
EMERGENCY SURGICAL EXPLORATION
Symptoms >24h
or atypical age or atypical clinical sign
Consider DDx*2
Torsion excluded*3,
consider DDx*2
*2 DDx:
Intermittent testicular torsion
Testical /epididymal appendix torsion
Epididymitis / Epididymo-orchitis
Scrotal edema, Tumour, others …
If NO delay in treatment
Emergency inguinal & scrotal US (US + C/DDS)
Torsion confirmed or equivocal US
* Typical clinical signs:
Sudden onset
Nausea and/or vomiting
Absent cremasteric reflex
High position of testis
*1 Manual detorsion:
Preferably US-guided.
If non-guided: Outwards rotation of testis unless pain increases or obvious resistance
Pediatr Radiol 2015; 45:2023-2028
Consider manual detorsion of testis*1
Abbreviations: CDS = Colour Doppler Sonography, DDS = Duplex Doppler Sonography, DDx = differential diagnosis,, US = ultrasound (high resolution, linear transducer!)
*3 Criteria: normal & symmetrical echogenicity & structure + symmetrical low resistance intratesticular arterial flow + normal course of spermatic cord (no whirlpool or spiral sign)

## Slide 35
Suspected testicular torsion in teenagers & young adults
(>10 years)
Typical clinical signs*
IMMEDIATE SURGICAL EXPLORATION
Doubtful signs
Inadequate examination due to inflammatory scrotal swelling
Normal spermatic cord with normal or increased flow
Intermittent testicular torsion?
Testical or epididymal appendix torsion?
Epididymitis / Epididymo-orchitis?
If NO delay in treatment
Lack of or reduced flow
Twisted spermatic cord
Testicular + spermatic cord assessment (US + C/DDS)
or
Pediatr Radiol 2015; 45:2023–2028
Consider manual detorsion of testis*1
Abbreviations: CDS = Colour Doppler Sonography, DDS = Duplex Doppler Sonography, US = ultrasound (high resolution, linear transducer!)
* Typical clinical signs:
Sudden onset
Nausea and/or vomiting
Absent cremasteric reflex
High position of testis
*1 Manual detorsion:
Preferably US-guided.
If non-guided: Outwards rotation of testis unless pain increases or obvious resistance

## Slide 36
Imaging algorithm in childhood ovarian torsion
Acute onset lower abdominal pain, but symptoms may be non-specific
Emergency laparoscopy
Transabdominal US (full bladder)
no suspicion*1
If NO delay in treatment
suggestive of ovarian torsion*
inconclusive
* Suggestive findings:
Heterogeneous enlarged ovary, possibly with mass lesion
Multiple (small) peripheral follicles
Fluid-debris levels within these cysts
Whirlpool sign
*1 No suspicion:
Normal & symmetric size, shape, echogenicity and position of ovaries
No ascites.
Pediatr Radiol 2017; 47:1369–1380
Abbreviations:, US = ultrasound
Note: neonatal ovarian torsion rare, with obscure symptoms & findings, mostly due to cysts. Check also for ovary within an inguinal hernia
other diagnosis
Consider alternate imaging
Persistent pain
Pain resolved
Observe
Beware of intermittent or partial torsion
Manage as appropriate

## Slide 37
Imaging in infants with disorders of sexual development
Pediatr Radiol 2015; 45:2023–2028
Abbreviations:, (ce-)US = (contrast enhanced ) ultrasound, MRI = magnetic resonance imaging
Clinical suspicion
Detailed transabdominal US (full bladder) + perineal US*
Sufficient - diagnostic
Inconclusive – equivocal or insufficient
*Assess:
Inner & outer genital structures / regions
  Labia, inguinal regions, retrovesical space
  Uterus? gonads? (normal ovaries/ testes, streak gonads )
Entire urinary tract
  include adrenal glands & urethra
*1 Imaging methods: (ce-)US genitography &/or fluoroscopic genitography, genital MRI, possibly MRI of other body areas (e.g., brain)
Depends on presentation & age, clinical & genetic findings
Always meticulous clinical / physical inspection
Additional imaging as needed *1
complex genital malformation
ambiguous genitalia with equivocal US
central hormone problem
Stop
Only potential clinical emergency: adrenal hyperplasia, severe dilatation / obstruction of urinary or genital tract

## Slide 38: Renal transplantation in childhood: pre-transplant imaging
Abbreviations: CDS = colour Doppler sonography, ce-CT = contrast enhanced CT, ce-VUS = contrast enhanced voiding urosongraphy, CTA/U = computed tomography angiography / urography, MRA/U = magnetic resonance angiography / urography, US = ultrasound, VCUG = voiding cystourethrography, VUR = v esico-ureteric reflux
Pediatr Radiol 2012; 42:
Pre-transplant imaging
Donor evaluation
Recipient evaluation
* US also includes pelvis &native kidneys
living
deceased
US & CDS of kidneys
ce-CT, if cerebral CTA performed to assess brain death
US & CDS of kidneys
+ MRA/U or CTA/U
  abnormal parenchyma on MR or US = baseline DMSA
Chest film
Abdominal US* & CDS
MR(A) if suboptimal visualization of vascular anatomy on US
Urodynamics /VCUG (ce-VUS)
Particularly vessel anatomy
  plan anastomosis
  if US insufficient = MRA/V
  Bladder assessment
  capacity, function, anatomy, VUR(?)
  Imaging of underlying conditions

## Slide 39: Renal transplantation in childhood: post-transplant imaging
Pediatr Radiol 2012; 42:
US* & (a)CDS/DDS
no complications / normal
Doppler anomalies
* US also includes pelvis &native kidneys
fluid collections
Surgical intervention / PCN
MAG3 / fMRU
(Pyelography)
US-guided core biopsy
DSA / interventional radiology / surgery
observe
parenchymal anomalies *1
allograft dysfunction
signs for secondary malignancy / PTLD
PCD / fluid collections
urinary leak
obstruction
*1 Clinically exclude
infections (UTI, sepsis)
drug toxicity
hypovolaemia / low blood pressure
lymphocele
seroma
haematoma
Abbreviations: AVF = arteriovenous fistula, (a)CDS = (amplitude coded) colour Doppler sonography, CT(A) = computed tomography (angiography), DMSA = dimercaptosuccinidacid scintigraphy, DSA = digital subtraction angiography, MR(A) = magnetic resonance (angiography), (f)MRU = (functional)magnetic resonance urography, MAG3 = Ma- scintigraphy , PCD = pelvicaliceal distention, PCN = percutaneous nephrostomy, PTLD = post-transplant lympho-proliverative disease, US = ultrasound, UTI = urinary tract infection
AVF/pseudo-aneurysm
Venous / arterial impairment
infarction
observe
thrombosis
RASt
DMSA/MRA?
(MRA/CTA?)

## Slide 40
Abbreviations: CDS = colour Doppler sonography, ce-VUS = contrast-enhanced voiding urosonography, CT = computed tomography, CTA = CT-angiography,, DMSA = Tc99m Dimercapto-succinid acid renal scintigraphy, DSA = digital subtraction angiography, PTLD = post transplantation lymphoproloferative disease, MRI(U) = magnetic resonance imaging,(urography), MRA = MR-angiography,, Tdx = transplant, US = ultrasound, UTI = urinary tract infection
Pediatr Radiol 2012; 42: 1275-1283
Allograft dysfunction
UTI
Hypertension
Suspected PTLD
/ malignancy
Confirmed PTLD
/ malignancy
Tdx US+CDS
Tdx US+CDS
Tdx US+CDS
Tdx & abdominal* US+CDS
chest X-ray
chest CT, abdominal & pelvic MRI or CT
brain MRI (if positive lumbar puncture)
DMSA (after 6 months)
MAG3, MRU, PCN
biopsy
biopsy
DSA (MRA/CTA?)
drainage
*1confirm
*abdominal US = + pelvis + native kidneys
some do VCUG/ce-VUS
if supicious lesion
if abnormal (C)DS or severe hypertension
if obstructed *1
if dilatated
Post-transplant imaging in children: When to do what
if scar detected

## Slide 41: Post-transplant imaging in children: Routine follow-up
Abbreviations: (a)CDS = (amplitude coded) colour Doppler sonography, DDS = duplex Doppler sonography, DEXA = Dual Energy X-Ray Absorptiometry (bone densitometry), DMSA = Tc99m Dimercaptosuccinid acid renal scintigraphy, MRI = magnetic resonance imaging, US = ultrasound
Peri-operative | US & (a)CDS/DDS
1st week | US & (a)CDS/DDS * Baseline DMSA or MRI in patients with risk of parenchymal loss
3 weeks | US & (a)CDS/DDS
3 months | US & (a)CDS/DDS
6 months | US & (a)CDS/DDS + abdominal US *
12 months | US & (a)CDS/DDS + abdominal US * DEXA if on high steroid dose
anual | US & (a)CDS/DDS + abdominal US *
Note: protocol transplant biopsies vary, and necessity / benefit under discussion
* abdominal US includes also pelvis and native kidneys
Comment: role of MRI has yet to be determined,
also importance of VUR assessment & respective method or timing
Pediatr Radiol 2012; 42: 1275-1283

## Slide 42: Part III: Miscellaneous statements (listed in alphabetical order)
The aim is to
Communicate other important issues that have not been addressed by procedural recommendations & imaging algorithms
  to highlight the entire spectrum in GI & GU imaging, e.g., on
    grading of UTD / PCD
    use of Gadolinium in childhood
    usability of ce-US in childhood
    or standardising terminology
Give references of other important similar activities & publications in this field
  endorsed by the Task Force, e.g., on
    CDK imaging
    assessment of DSD
    or sectional imaging of bowel
Abbreviations: ce-US = contrast enhanced ultrasound, CDK = cystic kidney disease, DSD = disorders of sexual development, GI = gastro-intestinal, GU = genito-urinary, PCD = pelvi-calyceal distension, UTD = urinary tract dilatation

## Slide 43: Potential indications for ce-US in infants & children
Intracavitary
ce-VUS: assessment of VUR , rarer: uretha assessment, fistulae
other ce-US: US genitography & cloacal malformations
drain position / function / leakage (e.g., abscess, PCN, pleural effusion)
orally for upper abdominal gastrointestinal queries
e.g. malrotation? stenosis? connection between cavities)
rectally (enema) for stenosis or fistula
Intravenously
parenchymal abdominal organs: lesion detection / confirmation)
e.g., in tumour conditions & trauma
lesion characterisation: at present primarily in liver (e.g., DDx abscess–tumour, type of tumour)
in complicated cysts in various organs
perfusion assessment: organ vital & well perfused? (e.g., organ transplant, vessel patent?)
small vessel arrangement & vascularity
vessels: depiction (eg., TCI, transplant), anatomy & patency
DDx vascular versus other cystic structure
& to enable proper spectral Doppler analysis & good angle correction
Abbreviations: ce-US = contrast-enhanced ultrasound, ce-VUS = contrast-enhanced voiding urosonography, DDx = differential diagnosis, PCN = percutaneous nephrostomy, TCI = transcranial imaging
Pediatr Radiol 2012;42:1275-1283, updated 2014;44: 1478-1484; and 2018;48:1528-1536

## Slide 44: Gadolinium & NSF in children
What to consider for paediatric ce-MRI
Reconsider the need of (ce-)MRI - extended dedicated US may suffice
Identify patients at increased risk: various risk factors, particularly renal failure or immature kidneys (neonates), acidosis, inflammation, dehydration, liver transplantation –
  GFR measurement / estimate (use paediatric Schwarz formula for GFR calculation, age/weight adapted creatinine normal values), creatinine/GFR mandatory with potential renal disease
reconsider ce-MRI (GFR <30), get informed consent, talk to nephrologist
Use only macrocyclic stable compounds registered for paediatric (neonatal) applications
Use supportive measures for prevention
  improve renal function & hydration, balance acidosis; BUT: no guaranteed security
Avoid repetitive application(s) - use only single dose, brake between repeated applications
record cumulative Gd dose (patient chart …)
Never deny a child an indicated ce-MRI study - if therapeutically necessary
Abbreviations: (ce-)MRI = (contrast-enhanced) Magnetic Resonance Imaging, Gd = Gadolinium, GFR = glomerular filtration rate, US = ultrasound
Pediatr Radiol 2009:39, update 2018;48: 1528-1536

## Slide 45: US grading of PCD / UTD in neonates & infants
Abbreviations PCD = pelvi-caliceal distention / dilatation, US = ultrasound, UTD = urinary tract dilatation
Pediatr Radiol 2008;38:1138-145, updated Pedaitr Radiol 2017;47:1369-1380
PCD 0 = collecting system not or hardy visible, normal
PCD I = just renal pelvis clearly visible, calices not depictable, axial pelvic diameter less than 7 mm, considered normal
PCD II = axial renal pelvis diameter less than 10 mm (some) calices visible, but with normal forniceal and papillar shape / configuration
PCD III = marked dilatation of calices and pelvis, the pelvic axial width usually >10 mm with flattened papilla and rounded fornices, but without parenchymal narrowing
PCD IV = gross dilatation of entire collecting system + narrowing of renal parenchyma
(PCD V = additionally used in some places, to communicate an extreme PCD IV° with only thin, membrane-like residual renal parenchymal rim
Modified from the ESPR „Hydronephrosis“ grading (Riccabona et al. 2008) - based on Hofmann‘s US grading, & the SFU classification (Fernbach et al. 1993)
Note: alternate grading system from America – „UTD classification system“ by Nguyen et.al, 2014, also addressing ureteral & fetal findings

## Slide 46: Typical US appearances in Cystic Kidney Disease (CKD)
Abbreviations: DD = differential diagnosis, US = ultrasound
Pediatr Radiol 2012; 42: 1275-1283
Adapted from Pediatric Urogenital Radiology, 3rd edition, Springer 2019
complicated cyst
  criteria : multilocular, (thick) septa, mass effect, nodular component, mass effect - resembling a Bosniak II-IV cyst
  cystic renal tumors
calyceal diverticula/tertiary calyx
DD urinoma, parapelvic cyst …
Schematic drawing of renal cysts with US & some histology representation

## Slide 47: Imaging in suspected childhood cystic kidney disease
Abbreviations: DDx = differential diagnosis, GN = glomerulonephritis, HUS = haemolytic-uremic syndrome, MCDK = multicystic dysplastic kidney, US = ultrasound
Pediatr Radiol 2012; 42: 1275-1283
US= hyperechoic or cystic kidneys
In setting of query „cystic disease“
other conditions with similar US finings unlikely
e.g., GN, HUS, renal vein thrombosis, shock …
family history
recurrence
isolated finding
Complementary examinations
DDx & follow-up (US)
NO
polymalformation Sy
YES
obstructive dysplasia / MCDK,
(segmental) dysplasia,
congenital reflux nephropathy …
typical US aspect
simple / acquired cyst
atypical US aspect
DDx & follow-up (US)
diagnosis

## Slide 48: CKD – when to do what
Abbreviations: ACKD = acquired cystic kidney disease, ACKD = acquired cystic kidney disease, ADTCDK = autosomal dominant tubule-cystic kidney disease, AML= angiomyolipoma, ARPKD = autosomal recessive polycystic kidney disease, BBS = Bardet-Biedl Syndrome, CGS = contiguous gene deletion syndrome, MCDK = multicystic dysplastic kidney, (ce-)MRI =(contrast-enhanced) magnetic resonance imaging, rTx = renal transplant, TSC = tuberous sclerosis, (ce-)US = (contrast-enhanced) ultrasound
Radiology 2019; 290:769–782
Prenatal suspicion of CDK | regular US monitoring, multidisciplinary care in pregnancy & post-natally
(Single) simple cyst | detailed medical & family history, thorough clinical examination, at least one follow-up US assessment – no CEUS, MRI or CT
Cystic dysplasia or MCDK | 
Bilateral cystic dysplasia or unilateral cystic dysplasia/MCDK without contralateral compensatory hypertrophy | at risk of progressive kidney disease: nephrological/clinical follow up, only little contribution of imaging = imaging follow-up not necessary (unless other reasons)
Unilateral cystic dysplasia or MCDK with contralateral hypertrophy | serial US to ensure continued appropriate compensatory hypertrophy If uncomplicated, no need to monitor MCDK itself
ARPKD - confirmed | annual abdominal US (portal hypertension; kidney size if severe & progressive)
only positive family history | imaging under discussion – clinical & therapeutic impact?
ADPKD - confirmed or suspected | confirmatory US within 12 months of initial screening; multiple cysts and/or enlarged kidneys = serial renal US, MRI if US restricted / research, > 15y
(Classical & CGS) TSC | Annual renal US for follow-up until puberty, (unenhanced) MRI thereafter initial MRI as part of work-up for atypical sonographically invisible AML?
Acquired cystic kidney disease | Annual US follow-up of native kidneys in patients on dialysis & after rTx No need in others once stable &/or known (post-traumatic)
Nephronophthisis | Regular kidney imaging not required; US for hepatic fibrosis in genetic defects associated with liver involvement
ADTCKD former “medullary cystic kidney disease” or “medullary sponge kidney” | Not defined – maybe annual US, or only if symptomatic? need for plain film or CT?
BBS, HNF1B disease also includes former „glomerular-cystic kidney disease“ | Depends on UT involvement; eg. regular US in BBS with significant abnormalities
Complicated cyst | ce-MRI, if US (including CEUS) is unable to classify
Cystic tumour | (CE)US + sectional contrast enhanced imaging, preferably MRI

## Slide 49: Standardised terminology in paediatric urogenital radiology
Correct terms | Definition | Not to confuse with/wrong terms
Duplex kidney/system | General term corresponding to complete (ureteral) or partial (bifid ureter) ) duplication | ureteral duplication bifid ureter
Ectopic ureterocele (by imaging) | Ureterocele that opens anywhere except in lateral trigone hardly seen by imaging. In practice, opening anywhere else than above bladder neck = in bladder neck or urethra | 
High grade vesico- ureteric reflux | Ureteral dilatation due to vesico-ureteric reflux (≥ grade III) | refluxing megaureter
Intravesical ureterocele | Ureterocele that opens into bladder proximal to bladder neck. | orthotopic ureterocele
Overactive bladder (OAB) | Term reserved when urodynamic test has been performed. Patient complains of urgency to void (bladder instability). | bladder instability.
Renal moiety | Renal (upper or lower) in case of duplex kidney | renal pole
Renal pole | Upper or lower extremity of renal parenchyma. | renal moiety
Transient echogenicity of the papillae | Transient increase in echogenicity of pyramids in postnatal period | Tamm-Horsfall proteinuria
Ureteral/ureteric duplication (duplicated ureter) | Two separate ureters (with 2 pelves) drain the urine of the same kidney with two vesicoureteral junctions. | bifid ureter duplex kidney duplex system
 | Recommended terms | Terms to avoid
Dilatation of |  | 
Calyces | Caliceal dilatation | Calicectasis Caliectasis
Calyces+pelvis* | Pelvicaliceal dilatation | Pelvocaliectasis Pyelocaliectasis
Pelvis alone | Pelvic dilatation | Pelviectasis Pyelectasis
Calyces + pelvis + ureter | Dilated urinary tract | 
Ureter alone | Ureteral dilatation Dilated ureter | Megaureter Ureterectasis
These terms are solely descriptive. None of them means that an obstruction is present. * UTD/PCD-grading should be provided according to the SFU classification. |  | 
Pediatr Radiol 2014; 44: 1478–1484and Pediatr Radiol 2018; 48:291-230
Abbreviations PCD = pelvi-caliceal distention / dilatation, SFU = Society for fetal urology, US = ultrasound, UTD = urinary tract dilatation

## Slide 50: Standardised terminology in paediatric urogenital radiology
Terms to avoid | Comments
Adult or simple ureterocele | Was used to describe single system ureterocele. Ureteroceles are congenital, can be found in single system & in children as well as adults. Simple implies inappropriately judgment of benignity.
Caecoureterocele | Was used to describe an intravesical ureterocele with extension into urethra during micturition. Prefer the term intravesical ureterocele with urethral prolapse.
Complex ureterocele | Implies inappropriately judgment of complexity or gravity. Was used to describe a ureterocele in association with a duplex kidney.
Double kidney | Was used to describe a duplex kidney. However, this term could implicate two identical units while in a duplex kidney the lower moiety is embryologically larger than the upper.
Megacystis-Megaureter syndrome | Was used to describe morphologic changes related to bilateral high grade grade VUR. Prefer this latter term.
Megaureter | Misleading as it should always be prefaced with the terms "primary", or "secondary", or refluxing. When describing a dilated ureter without knowing the etiology, this term should be avoided. If cause unknown, the term dilated ureter if any or more simply dilated ureter should be used.
Sphincteric ureterocele | Was used to describe a patulous orifice distal to the bladder neck. Simply describe it as a urethral ureterocele.
Sphincterostenotic ureterocele | Was used to describe a sphincteric and stenotic ureterocele. Both terms should be avoided as this one.
Stenotic ureterocele | Was used to describe a intravesical ureterocele with a narrow opening. But, ureterocele is caused by a narrow opening (with or without true chronic obstruction).
Tamm-Horsfall proteinuria (in case of hyperechogenicity of papillae in neonatal period) | Was used to describe transient echogenicity of the papillae. It was thought that Tamm-Horsfall proteinuria was responsible for this ultrasonographic pattern. It turned out to be wrong.
Pediatr Radiol 2014; 44: 1478–1484and Pediatr Radiol 2018; 48:291-230
Abbreviations VUR = vesico-uretric reflkux

## Slide 51: Summary & conclusion
The Task Force has issued numerous recommendations
for paediatric GI & GU imaging
  after identifying fields where homogenisation of imaging seemed essential
  where definition of standards was necessary
  to ease access to information for everybody who is involved with imaging children & to provide high quality imaging
  to empower everybody to propose the proper imaging options & algorithms
By this the Task Force tried to contribute to improve imaging
of the child’s GI & GU tract
  additionally lay the base for providing comparable data for future research helping to then create more evidence based recommendations
The success of this endeavour heavily relies on
  usage & application of these recommendations which again needs awareness, wide distribution & easy access - hopefully promoted by this summary
  discussion & future developments are essential & adaptations will be necessary
  everybody welcome to comment & get involved

## Slide 52
Literature list – Task force (& related) publications
Riccabona M, Avni FE, Blickman JG, Darge K, Dacher JN, Lobo LM, Willi U (2008) Imaging recommendations in paediatric uroradiology: Minutes of the ESPR workgroup session on urinary tract infection, fetal hydronephrosis, urinary tract ultrasonography and voiding cysto-urethrography. ESPR-Meeting, Barcelona/Spain, June 2007. ESUR Paediatric guideline subcom-mittee and ESPR paediatric uroradiology work group. Pediatr Radiol 38: 138-145
DOI: 10.1007/s00247-007-0695-7
Riccabona M, Avni FE, Blickman JG, Dacher JN, Darge K, Lobo ML, Willi U. (Members of the ESUR paediatric paediatric recommendation work group and ESPR paediatric uroradiology work group) (2009). Imaging recommendations in paediatric uroradiology, part II: urolithiasis and haematuria in children, paediatric obstructive uropathy, and postnatal work-up of foetally diagnosed high grade hydronephrosis. Minutes of a mini-symposium at the ESPR annual meeting, Edinburgr June. Pediatr Radiol 39 (8): 891-898 DOI 10.1007/s00247-009-1233-6
Riccabona M, Avni FE, Dacher JN, Damasio B, Darge K, Lobo ML, Ording-Müller LS, Papado-polos F, Willi U. (2010). ESPR uroradiology task force and ESUR paediatric working group: Im-aging and procedural recommendations in paediatric uroradiology, Part III. Minutes of the ESPR uroradiology task force mini-symposium on intravenous urography, uro-CT and MR-urography in childhood. Pediatr Radiol 40 (7): 1315-1320
Riccabona M, Avni F, Dacher JN, Damasio B, Darge K, Lobo ML, Ording-Müller LS, Papado-poulou F, Vivier P, Willi U. (2011). ESPR uroradiology task force and ESUR paediatric working group: imaging recommendations in paediatric uroradiology, part IV Minutes of the ESPR uro-radiology task force mini-symposium on imaging in childhood renal hypertension and imaging of renal trauma in children. Pediatr Radiol 41 (7): 939-944 DOI: 10.1007/s00247-011-2089-0
Riccabona M, Avni F, Damasio B, Ordning-Mueller LS, Lobo ML, Darge K, Papadopoulou F, Willi U, Blickmann J, Vivier PH. (2012) ESPR Uroradiology Task Force and ESUR Paediatric Working Group - Imaging recommendations in Paediatric Uroradiology, Part V: Childhood cystic kidney disease, childhood renal transplantation, and contrast-enhanced ultrasound in children. Pe-diatr Radiol 42: 1275-1283 DOI: 10.1007/s00247-012-2436-9
Riccabona M. (2012) Application of a second generation ultrasound contrast agent in infants and children – a European questionnaire-based survey. Pediatr Radiol 42(12):1471-1480 DOI: 10.1007/s00247-012-2472-5
Damasio M, Darge K, Riccabona M. (2012/13). Multi-detector CT in the paediatric urinary tract. EJR - Europ J Radiol 82: 1118- 1125; Doi:10.1016/j.ejrad.2011.12.005
Riccabona M, Lobo ML, Willi U, Avni F, Blickmann J, Damasio B, Ordning-Mueller LS, Darge K, Papadopoulou F, Vivier PH. (2014) ESPR Uroradiology Task Force and ESUR Paediatric Working Group - Imaging recommendations in Paediatric Uroradiology, Part VI: Childhood renal biopsy and imaging of neonatal and infant genital tract. Pediatr Radiol 44: 496-502 DOI: 10.1007/s00247-013-2852-5
,

## Slide 53
Riccabona M, Vivier HP; Ntoulj A; Darge K, Avni F; Papadopoulou F; Damasio B; Ording-Mueller LS; Blickman J; Lobo ML; Willi U. (2014) ESPR Uroradiology Task Force – Imaging Recommendations in Paediatric Uroradiology - Part VII: Standardized terminology, impact of ex-isting recommendations, and update on contrast-enhanced ultrasound of the paediatric urogenital tract. Pediatr Radiol 44:1478-1484, Epub 2014 Oct 21 doi: 10.1007/s00247-014-3135-5.
Riccabona M, Darge K, Lobo ML, Ording-Muller LS, Augdal TA, Avni FE; Blickman J; Damasio BM; Ntoulia A, Papadopoulou F, Vivier PH; Willi U (2015) ESPR Uroradiology Task Force – Im-aging Recommendations in Paediatric Uroradiology - Part VIII: Rethrograde urethrography, imag-ing in disorders of sexual development, and imaging in childhood testicular torsion. Report on the mini-symposium at the ESPR meeting in Amsterdam, June 2014, Pediatr Radiol 45, DOI: 10.1007/s00247-015-3353-5
Riccabona M; Lobo ML, Ording-Muller LS, Augdal TA, Avni FE, Blickman J, Bruno C, Dama-sio B, Darge K, Ntoulia A, Papadopoulou F, Vivier PH. (2017). ESPR Abdominal (GU and GI) Imaging Task Force – Imaging Recommendations in Paediatric Uroradiology, Part IX: imaging in anorectal and cloacal malformation, imaging in childhood ovarian torsion, and efforts in standard-ising pediatric uroradiology terminology. Report on the mini-symposium at the ESPR meeting in Graz, June 2015. Pediatr Radiol, 47:1369-1380. doi: 10.1007/s00247-017-3837-6. Epub 2017 Aug 29.
Damasio B, Ording-Mueller LS, Piaggio G, Marks St, Riccabona M (2017). Imaging in paediatric renal transplantation. Pediatr Transplantation 21 (3) Doi:10.1111/petr.12885. PubMed PMID: 28121050.
Riccabona M, Lobo ML, Augdal ThA, Avni FE, Blickman J, Bruno C, Damasio MB, Darge K, Mentzel HJ, Napolitano M, Ntoulia A, Papadopoulou F, Petit Ph, Woźniak MM, Ording-Mueller LS (2018). ESPR Abdominal (GU and GI) Imaging Task Force - Imaging Recommendations in Paediatric Uroradiology, Part X: How to perform paediatric gastrointestinal ultrasonography, use of Gadolinium as a MRI contrast agent in children, follow-up of paediatric testicular microlithiasis, and update in paediatric contrast-enhanced ultrasound. Report on the task force session at the ESPR meeting in Davos, June 2017. Pediat Radiol 48, 1528–1536 (e-pub Juni 2018)DOI: 10.1007/s00247-018-4147-3
Vivier PH, Augdal TA, Avni FE, Baccheta J, Beetz R, Bjerre AK, Blickman J, Cochat P, Coppo R, Damasio B, Darge K, El-Ghoneimi A, Hoebeke P, Läckgren G, Leclair MD, Lobo ML, Manzo-ni G, Marks SD, Mattioli G, Mentzel HJ, Mouriquand P, Nevéus, T, Ntoulia A, Ording-Muller LS, Oswald J, Papadopoulou F, Porcellini G, Ring E, Rösch W, TeixeiraAF, Riccabona M. (2017/2018) Standardization of pediatric uroradiological terms: a multidisciplinary European the-saurus. J Pediatr Urol 2017; 13:641-650 , doi: 10.1016/j.jpurol.2017.05.026 und Pediatr Radiol 2018; 48:291-303 doi: 10.1007/s00247-017-4006-7
Watson T, Petit Ph, Augdal TA, Avni EF, Bruno C, Damasio M.B, Darge K, Kjucevsek D, Fran-chi-Abella St, Ibe D, Littooij A, Lobo ML, Mentzel JH, Napolitano M, Ntoulia A, Riccabona M, Stafrace S, Wozniak M, Ording Müller LS (2019). European Society of Paediatric Radiology Ab-dominal Imaging Task Force: Statement on Imaging in Very Early-onset Inflammatory Bowel Dis-ease. Pediatr Radiol 49 (6):841–848; https://doi.org/10.1007/s00247-019-04421-5
Avni FE, Lerisson H, Lobo ML, Cartigny M, Napolitano M, Menzel HJ, Riccabona M, Wozniak M, Kljucevsek D, Augdal TA, Bruno C, IbeD, Darge D, StafraceS, Ph, Ording Muller LS (2019). Disorders of sex development in neonates: plea for a standardized imaging approach: plea for a standardized imaging approach. Pediatr Radiol 49:1240-1247; doi: 10.1007/s00247-019-04414-4

## Slide 54
Damasio MB, Ording Müller LS, Augdal TA, Avni FE, Basso L, Bruno C, Ključevšek D, Littooij AS, Franchi-Abella S, Lobo LM, Mentzel HJ, Napolitano M, Ntoulia A, Riccabona M, Stafrace S, Woźniak MMM, Petit P. (2019/20)European Society of Paediatric Radiology abdominal imaging task force: recommendations for contrast-enhanced ultrasound and diffusion-weighted imaging in focal renal lesions in children. Pediatr Radiol. 2020; 50:297-304. doi: 10.1007/s00247-019-04552-9. Epub 2019 Nov 27. PubMed PMID: 31776600.
Kjucevsek D, Riccabona M, Petit Ph, Avni EF, Bruno C, Damasio M.B, Darge K, Littooij A, Lobo ML, Mentzel JH, Napolitano M, Wozniak M, Ording Müller LS (2020). Intracavitary contrast-enhanced Ultrasound in children: A review, with clinical applications and procedural recommendations from the ESPR Abdominal Task Force Group. Pediatr Radiol 50. E-published Febr. 2020; doi.org/10.1007/s00247-019-04611-1
Napolitano M, Franchi-Abella S, Damasio BM, Augdal TA, Avni FE, Bruno C, Darge K, Ključevšek D, Littooij AS, Lobo ML, Mentzel HJ, Ntoulia A, Riccabona M, Stafrace S, Toso S, Woźniak MM, DiLeo G, Sardanelli F, Ording Müller LS, Petit P (2020). Practical approach for the diagnosis of biliary atresia on imaging: an up-date and guidelines from the ESPR. Part 1: Prenatal US and MRI and postnatal US diagnosis. Pediatr Radiol
,

## Slide 55: Other (consensus) statements from/with TF involvement
Imaging cystic kidney disease: Imaging of kidney cysts and cystic kidney diseases in children. An International Working Group consensus statement. Radiology 2019; 290:769–782
Imaging for testicular microlithiasis: “ … For follow-up of children with testicular microlithiasis, we
recommend considering regular US even in isolated testicular microlithiasis as the association between testicular microlithiasis and malignant tumours in children cannot be neglected. …“ Pediatr Radiol 2018;48:1528–1536
Imaging in DSD: Plea for a standardized imaging approach to disorders of sex development in neonates: consensus proposal from European Society of Paediatric Radiology task force; Pediatr Radiol 2019;49:1240-1247
Sectional imaging for bowel disease: The first joint ESGAR/ ESPR consensus statement on the technical performance of cross-sectional small bowel and colonic imaging. Europ Radiol 2017; 27:2570–2582
Renal imaging: Recommendations for contrast-enhanced ultrasound and diffusion-weighted imaging in focal renal lesions in children. Pediatr Radiol 2020; 50:297-304
Imaging in NSF: Gadolinium and Nephrogenic Systemic Fibrosis; Pediatric Uroradiology, Springer 2008; pp 515-517
Contrast agents in childhood: Contrast media use in pediatrics: safety issues. Contrast Media Safety Issues and ESUR Guidelines, Springer 2014: pp 245-253
Standardised paediatric uroradiology terminology: Standardization of pediatric uroradiological terms: a multidisciplinary European thesaurus. Pediatr Radiol 2018; 48:291-230